## Slide 1: A.S.T.R.O.COM. Advanced Solar Tracking and Rover Observation Communication
Alex Fiset | Pedro Kasprzykowski | Stephen Martin | Binh Pham
Electrical Engineering | Computer Engineering | Computer Engineering | Computer Engineering
Project sponsored by Florida Space Institute (FSI)

## Slide 2: Motivation and Background
South Pole of Moon is area of interest for researchers
Lunar south pole has many craters that are in permanent darkness due to the sun's path across the lunar south pole's sky
Approached by FSI to solve a few problems for lunar exploration:
  Permanently dark locations on the moon are difficult to explore
    Lack of power infrastructure on the moon limits exploration
    Permanently dark locations are a valuable location for research
  Communication on lunar surface is limited
    Range of communication limits exploration of craters
    Limited communication infrastructure on moon

## Slide 3: Motivation and Background
Proposed Solution:
  A heliostat tower
    To reflect light from the sun into permanently dark locations
    Equipped with communication capabilities
  A smaller communication beacon
    Carriable by rovers
    Form a communication network with rovers

## Slide 4: Goals
Overall Goals (High Level)
Build a tower to handle rover communication.
Build a tower to handle sunlight diversion to targets.
Stretch Goals
P2P Networking for communication and mirror tower with rovers.
Wireless charging and/or docking station for communication tower.

## Slide 5: Objectives
Mirror Tower Objectives (Lower Level)
Identify optimal sun location based on lux value from sensor.
Receive requests from communication tower using protocols.
Create a heliostat algorithm to orient towards the target with motors.
Create a self-sustainable power supply using solar and battery power.
Communication Beacon Objectives (Lower Level)
Receive requests from target through mesh network protocols.
Relay requests to mirror tower using communication protocols.
Create a small and portable tower that can be moved by rovers.

## Slide 6: Specifications Table
Heliostat Tower | 
Minimum Temperature | -40°C
Reflector | 
Minimum Reflectivity | 90%
Response Time | 3 minutes
Solar Panel | 
Minimum Power | 30W during sunlight hours
Maximum Voltage | 24V
Battery | 
Minimum Lifespan | 2 weeks without sun
Communication Tower | 
Minimum Network Range | 20m
Communication Rate | 2400MHz
Maximum Current Draw | 500mA
Latency | 1 second
Maximum Power | 5W
  A heliostat tower
    Respond time to change reflection target estimated to be maximum 3 minutes
    Minimum power can be usage to all component estimated to be 30W
  Communication tower
    Maximum power usage estimated to be 5W

## Slide 7: Hardware Block Diagram

## Slide 8
Software Block Diagram
Fully integrated code software flowchart
  Perspective of Mirror Tower
  Yellow is signal from Communication Beacon

## Slide 9: MICROCONTROLLER UNIT
 | ESP32 | MSP430 | Raspberry Pi 0 | Arduino MKR1310 | Arduino MK1010
Cost (USD) | 9.18 | 20 | 15 | 46 | 38.6
Zigbee | Yes | No | Yes | No | No
I2C | Yes | Yes | Yes | Yes | Yes
Flash Memory | 4 MB | 128 KB | None | 256 KB | 256 KB
RAM | 520 KB | 2 KB | 512 MB | 32 KB | 32 KB
Power (W) | 1.3644 | 1 | 12.5 | 0.5082 | 0.5082
Microcontroller was chosen over FPGA
  Low power consumption, cost, and high amounts of documentation.
ESP32 is low cost, low power and networking capabilities and all connections required.

## Slide 10: Solar Panels
Model | RNG-50D-SS | HQST-50P-US | SP-52-L
Brand | Renogy | HQST | Solbian
Technology | Monocrystalline | Polycrystalline | Monocrystalline
Price | $ 59.99 | $ 65.99 | $ 499.00
Pmax at STC | 50 W | 50 W | 52 W
Voc | 22.3V | 23.3V | 10.9V
Vmp | 18.6V | 19.8V | 9.1V
Imp | 2.69A | 2.53A | 5.7A
A monocrystalline 50W panel from Renogy was selected due to the low cost and high performance.

## Slide 11: Voltage Regulation
Specifications | Linear Regulators | Switching Regulators |  | 
 |  | Buck | Boost | Buck-Boost
Efficiency | Moderate | High |  | 
Heat | Moderate | Low |  | 
Voltage Output | Step-Down | Step-Down | Step-Up | Up or Down
Output Ripple | Low | Low | High | Low
Complexity | Low | Moderate | Moderate | High
Cost | Low | Moderate | Moderate | High
Switching Buck regulators were chosen for their simplicity and low cost, being commercially available cheaply from many manufacturers.

## Slide 12: Voltage Regulation
Model | LM1085IT-5.0/NOPB | DROK MiniBuck Converter | LM2596 | TPS54JA20
Brand | Texas Instruments | DROK | Texas Instruments | Texas Instruments
Input Voltage | 2.6-26V | 2.5-24V | 3-40V | 2.7–16V
Output Voltage | 3.3 or 5 | 3.3 or 5 | 1.5 to 35 | 0.5 to 5.5V
Output Current | 3A | 3A | 3A | 12A
Price | 2.19 | 1.97 | 1.495 | 0.65
Type | LDO Buck | Buck | Buck | Buck
The TPS53JA2 was selected due to the high output current, supported the intended voltage input, and was high efficiency.

## Slide 13: Charge Controller
Two broad categories of Solar Charge Controllers:
  PWM
    Basic pulse width modulation
    Lower efficiency
    Cheaper
  MPPT
    Tracks highest power producing operating point
    Higher efficiency
    Typically, more expensive

## Slide 14: Charge Controller
Model | BQ25798RQMR | SR11004 | Adventurer
Brand | Texas Instruments | SMARAAD | Renogy
Input Voltage | 24V max | 26V max | 50V max
Output Voltage | 18.8V max, Programmable | 12/24V | 12/24V
Output Current | 5A | 10A | 30A
Price | 6.25 | 39.99 | 59.99
Power | Not Specified | 260W | 1500W
Type | MPPT | MPPT | PWM
The SR11004 from SMARAAD offered the right voltage output, and was compatible with the selected battery chemistry for the lowest price.

## Slide 15: Reflectors
Material Chosen to fabricate:
Aluminum: high heat resistance, durable, and high reflectivity in the moon environment.
Mylar: increase reflectivity, high heat change resistance, won’t crack, and don’t reduce quality of refection
Proof of concept: Acrylic panel as cheaper alternative and easier to fabricate.

## Slide 16: Motors
Stepper motor: Nema 23 robustness and strong torque to control the rotation of the whole tower. Can be used on DC system
Servo Motors: a cheaper alternative for smaller part movements.
Incorporated gearbox to increase movement range and control for stepper motor.
Types of Motors | AC | Stepper | Servo
Financial Cost | $200-$2,000 | $20-$200 | $10-$50
Torque | 203000Ncm-610000Ncm | 10-10000Ncm | 10-1000Ncm
Speed | 1800-3600 rmp | Low | High
Voltages requirement | 115V/208V/230V | 3V-100V | 3V-100V
Durability | High | High | Low

## Slide 17: Motor Controllers
Stepper Controller TB6560-V2, cheap and can handle the at least 2 amperage from Nema23
PCA9685 PWM: Design specific for servo and can control all three servos planned in the system
Controller Models | DRV8434S, 2A Max. | TB6560 | Stepper Motor Driver 36v4 | HiLetgo PCA9685
Cost (USD) | $12.95 | $11.39 | $29.95 | $9
continuous current (A) | 1.2 | 3.5 | 4 | 3A
Micro stepping | 1/256 | 1/16 | 1/256 | I2C
Operating Voltage (V) | 4.5-48 | 10-35 | 8-50 | 5-10

## Slide 18: Batteries
Model | ML5-12 | HW-4F7 | PQ12V/6AH
Brand | Mighty Max Battery | Howell Energy | Power Queen
Voltage | 12 | 12 | 12.8V
Amp Hour | 5 | 7 | 6
Technology | SLA AGM | LiFePO4 | LiFePO4
Price | 16.99 | 32.99 | 19.59
Charging Requirements | CV | CC 3.5A, CV 14.6V, Built-in BMS | Not Specified, Built in BMS
The battery selected was a Howell Energy LiFePO4 battery.
  Higher amp hours
  Lower weight
  Smaller size
  Higher price

## Slide 19: Antenna
 | PC140 | WPC.25A | FXP74 | PC17 | FXP70
Avg Gain (dB) | -1.92 | -1.14 | -2 | -3.6 | -2
Peak Gain (dBi) | 1.67 | 5.15 | 4 | .9 | 1.1
Efficiency (%) | 64 | 76.9 | 50 | 44 | 63.7
VSWR | <2 | <2 | <2 | <1.5 | <1.5
Polarization | RHCP | Linear | Linear | Linear | Linear
Cost (USD) | $27.26 | $9.21 | $7.69 | $16.60 | $27.09
The combination of the certain gain range, circular polarization, high-efficiency and wideband characteristics made patch and helical antenna types the ideal choices.
The PC140’s circular polarization while also being above average in gain and efficiency made it the preferred antenna product.
The sponsor chose for us to replace the antenna with their choice of the wlaniot.

## Slide 20: Sensor
 | VL6180X | MAX44009 | SI1145 | VEML7700
Cost (USD) | $14.49 | $5.96 | $9.95 | $4.95
Measuring Principle | TOF/IR Laser Photodiode | Photodiode | IR-LED Photodiode | Photodiode
Max Lux | 100000 | 188000 | 128000 | 120000
Ambient Light Sensing | Yes | Yes | Yes | Yes
Operating Current (mA) | 0.3 | 0.003 | 7 | 0.045
I2C | Yes | Yes | Yes | Yes
Sensor Final 4 Options:
VL6180X and SI1145 include IR which is not needed
MAX44009 only has breakout board; does not work for PCB
VEML7700 best choice for price/ability

## Slide 21: Development Environment: Languages and Repositories
Programming Languages
C: best choice for MCU programming, low-level
Java: best for object-oriented programming, low-level
Python: best for existing libraries, high-level
Choice: C
Repositories
GitHub: most popular repo, widely used among many software devs
Bitbucket: Git based repo, includes task scheduling and team goal software
Choice: GitHub

## Slide 22: Vectoring and Positioning / Solar Tracking Algorithm
Algorithms | Heliostat | Kalman Filtering | Ray Tracing
Financial Cost | Open Source | Ambiguous | Not available
Sensor | Ambient Light | Ambient Light | Ambient Light
Algorithm code library | Available on GitHub | Available in python | Available in Research paper
Efficiency | High | Low | Medium
MCU compatibility | Good (C Language) | Fair (Python) | Good (C Language)
Heliostat algorithm chosen as it is open source and availability. Good capability with ESP32-C6 and C language

## Slide 23: Communication technologies
Criteria | Wi-Fi | Bluetooth | Zigbee | Z-Wave
Range (m) | 45 | 10 | 980 | 800
Data rate | 54 Mbps | 1 Mbps | 250 Kbps | 100 Kbps
Power consumption | 30 uA-250 mA | 9 uA-39 mA | 12 uA- 54 mA | 1 uA-23 mA
Max devices | 255 | 3-4 | 100 | 232
Scalability | ✓ | ✖ | ✓ | ✓
Frequency | 2.4/5/6 GHz | 2.4 GHz | 915 MHz/2.4 GHz | 908-916 MHz
The combination of low power consumption, suitable range, options for frequency and high scalability made Zigbee the ideal communication technology to implement.

## Slide 24: Hardware Design
Design two separate towers, each with their own design constraints
Majority of focus is on heliostat tower, as it is more complex
Schematics and PCB designs
Heliostat structure
Tripod on a "Lazy Susan"
Communication Beacon
Antenna on an enclosure

## Slide 25: Power Delivery/ Electrical Power System

## Slide 26: Servo Motor Controls

## Slide 27: Sensor Control

## Slide 28: MCU System

## Slide 29: Lower-Level Subsystem

## Slide 30: Lower-Level Subsystem

## Slide 31: Power Control Algorithm
Component | Essential/Non-Essential | Low-Power Considerations
MCU | Essential | Low-Power Mode, only essential functions
Antenna | Essential | Receive only
Sensors | Essential | Sensors will be turned on periodically
Stepper Motor | Non-Essential | 
Servo Motors | Non-Essential | 
Goal was to reduce power consumption when the sun would not be visible
Reducing usage of non-essential components during these times would preserve battery charge

## Slide 32
MCU PCB

## Slide 33
MCU PCB

## Slide 34: Sensors PCB

## Slide 35: SErVo Motor controller PCB

## Slide 36: Software Design
Details on software design for the overall system which includes:
Communications through the mesh network
Collecting sensor information
Positioning reflector to deliver sunlight to target
Represented with software diagrams

## Slide 37
Case Diagram

## Slide 38
Activity Diagram

## Slide 39
Motor positioning of Reflector based on light intensity algorithm.

## Slide 40: Hardware testing
Tested components and had great success.
Did have a few issues during implementation including:
  Strapping pins and UART TX/RX mix-ups
  Higher than expected channel capacitance causing low rise time for I2C
  Voltage drop from servos, resetting the servo controller
These issues were resolved with a mix of software and hardware changes.

## Slide 41: Software testing
Transforming individual parts code to integrated code
  Included interrupts to handle events
  Sensors in certain locations are averaged and divided by each other to dynamically track movements
  Scaling operations were needed to transform step sizes from different servos
  Zigbee operations included to switch targets
Created our own coordinator for testing but will use rover from G16 in live demo
  This coordinator will relay information from communication box (Zigbee end device) to the reflector tower (Zigbee end device)

## Slide 42: Administrative Contents
Electrical Engineering | Responsibilities
Alexandre Fiset | PSU Design and Implementation
 | PCB Design
 | MPPT Tracking Implementation
 | Administrative Documentation
Computer Engineering | Responsibilities
Binh Pham | Reflector Technology and Design
 | Motor and Motor Controls
 | Vectoring Technology
 | Project Lead
 | Positioning and Vectoring Algorithm
Computer Engineering | Responsibilities
Pedro Kasprzykowski | MCU Selection and Implementation
 | Software Design and Implementation
 | Antenna and Communications
 | Website Design and Management
Computer Engineering | Responsibilities
Stephen Martin | Sensor Selection and Implementation
 | MCU Selection and Implementation
 | Positioning and Vectoring Algorithm
 | Software Design and Implementation

## Slide 43: Mechanical's Budgets
Component | Name | Price/unit | Quantity
Mirror | 0.032" x 24" x 24", 3003-H14 Aluminum Sheet | $28.86 | 1
Mirror Coating | Mylar Sheet | $25.99 | 1
Frame | ADJ LTS-6 T-Bar Tripod Lightweight Lighting Stand | $54.99 | 1
Base Panels | Plywood Panels 4ftx8ft | $25.60 | 2
Communication Tower Box | Junction Box | $26.89 | 1
Wheel Hub Bearing | Rear Wheel Hub | $44.90 | 1

## Slide 44: Electrical’s Budget
Component | Name | Price | Quantity
Battery | Howell Energy hw-4f7 | 32.99 | 1
Motor w | Nema 23 | $30.73 | 1
Motor x-y-z | 9.5-11kg*cm Servo Motor | $17.59 | 3
Charge Controller/BMS | Smaraad SR11004 | $39.99 | 1
Solar Panel | RNG-50D-SS | $49.99 | 1
Microcontroller | ESP32-C6-DEVKITC-1-N8 | $9.00 | 1
External Antenna | Wlaniot 2.4G | $17.98 | 2
MicroSD card | 5251 | $4.50 | 2
MicroSD card breakout board+ | 254 | $7.50 | 1

## Slide 45: PCB’s Budget
Component | Name | Price | Quantity
Microcontroller for PCB | ESP32-C6-WROOM-1U | $3.48 | 1
Stepper Motor Controller | DRV8833PW | $2.84 | 1
Servos Motor Controller | PCA9685PW,112 | $2.64 | 1
3.3V Regulator | TPS54JA20 | $1.50 | 1
5V Regulator | TPS54JA20 | $1.50 | 1
USB-A Connector | 2057-USB-AP-S-RA-SMT-ND | $0.55 | 3
Sensor-MUX | TCA9548APWR | $1.78 | 1
Sensor | VEML7700 | $1.88 | 5
USB-to-UART Bridge Controller | CP2102N-A02-GQFN28 | $4.07 | 1
MicroSD Socket | 1660 | $1.95 | 1
Misc. | Resistors, Capacitors, Inductr, Jumpers, Etc.…. | ~$20.00 |