## Slide 1: A.S.T.R.O.COM. Advanced Solar Tracking and Rover Observation Communication
Alex Fiset | Pedro Kasprzykowski | Stephen Martin | Binh Pham
Electrical Engineering | Computer Engineering | Computer Engineering | Computer Engineering

## Slide 2: Motivation and Background
South Pole of Moon is area of interest for researchers
Lunar south pole has many craters that are in permanent darkness due to the sun's path across the lunar south pole's sky
Approached by FSI to solve a few problems for lunar exploration:
  Permanently dark locations on the moon are difficult to explore
    Lack of power infrastructure on the moon limits exploration
    Permanently dark locations are a valuable location for research
  Communication on lunar surface is limited
    Range of communication limits exploration of craters
    Limited communication infrastructure on moon

## Slide 3: Motivation and Background
Proposed Solution:
  A heliostat tower
    To reflect light from the sun into permanently dark locations
    Equipped with communication capabilities
  A smaller communication beacon
    Carriable by rovers
    Form a communication network with rovers

## Slide 4: Goals
Overall Goals (High Level)
Build a tower to handle rover communication.
Build a tower to handle sunlight diversion to targets.
Stretch Goals
P2P Networking for communication and mirror tower with rovers.
Wireless charging and/or docking station for communication tower.

## Slide 5: Objectives
Mirror Tower Objectives (Lower Level)
Identify optimal sun location based on lux value from sensor.
Receive requests from communication tower using protocols.
Create a heliostat algorithm to orient towards the target with motors.
Create a self-sustainable power supply using solar and battery power.
Communication Beacon Objectives (Lower Level)
Receive requests from target through mesh network protocols.
Relay requests to mirror tower using communication protocols.
Create a small and portable tower that can be moved by rovers.

## Slide 6: Specifications Table
Heliostat Tower | 
Minimum Temperature | -40°C
Reflector | 
Minimum size | 1ft diameter
Maximum size | 5ft diameter
Maximum Weight | 9kgs
Minimum Reflectivity | 90%
Response Time | 3 minutes
Tower Frame | 
Maximum total weight | 27kgs
Minimum Weight Capacity | 10kgs
Solar Panel | 
Minimum Power | 30W during sunlight hours
Maximum Voltage | 24V
Battery | 
Minimum Lifespan | 2 weeks without sun
Communication Tower | 
Minimum Enclosure Volume | 6.5"x6.5"x5"
Maximum Weight | 2kg
Minimum Network Range | 20m
Communication Rate | 2400MHz
Voltage input | 3.3V or 5V
Maximum Current Draw | 500mA
Minimum Temperature | -40°C
Latency | 1 second
Maximum Power | 5W

## Slide 7: Hardware Block Diagram

## Slide 8: Software Block Diagram

## Slide 9: Comparison and Selection of Hardware
MCU
Solar Panels
Voltage Regulation
3Charge Controller
Reflectors
Motors
Motor Controllers
Sensor
Batteries
Antenna

## Slide 10: MCU
Criteria | Microcontroller | FPGA
Environmental robustness | ✓ | 
Low power consumption | ✓ | 
Parallel processing |  | ✓
Ease of use | ✓ | 
Processing power |  | ✓
Cost | ✓ | 
Scalability |  | ✓
Integration/Peripherals | ✓ | 
Documentation | ✓ | 
 | ESP32 | MSP430 | Raspberry Pi 0 | Arduino MKR1310 | Arduino MK1010
Cost - Processor & DevKit (USD) | 9.18 | 20 | 15 | 46 | 38.6
Wi-Fi | Yes | No | Yes | No | Yes
Bluetooth | Yes | No | Yes | No | Yes
Zigbee | Yes | No | Yes | No | No
Z-Wave | No | No | Yes | No | No
LoRaWAN | No | No | Yes | Yes | No
6LoWPAN | No | No | Yes | No | No
UART | Yes | Yes | Yes | Yes | Yes
I2C | Yes | Yes | Yes | Yes | Yes
SPI | Yes | Yes | Yes | Yes | Yes
PWM | Yes | Yes | Yes | Yes | Yes
ADC | Yes | Yes | Yes | Yes | Yes
DAC | Yes | Yes | No | Yes | Yes
Flash Memory | 4 MB | 128 KB | None | 256 KB | 256 KB
RAM | 520 KB | 2 KB | 512 MB | 32 KB | 32 KB
Operating Voltage (V) | 3.6 | 5 | 5 | 3.3 | 3.3
Current Draw (A) | 0.379 | 0.2 | 2.5 | 0.154 | 0.154
Power Consumption (W) | 1.3644 | 1 | 12.5 | 0.5082 | 0.5082
Microcontroller was chosen over FPGA, presenting characteristics that were better fits for the project such as low power consumption, cost and high amounts of documentation.
ESP32 had the best combination of low cost, low power and networking capabilities and all connections required.

## Slide 11: Solar Panels
Solar Panel Technology | Efficiency | Low-Light Perf. | Temp. Tolerance | Radiation Resistance | Degradation | Weight & Size
Monocrystalline | High | Excellent | Good | Good | Low | Relatively heavier
Polycrystalline | Moderate | Good | Good | Good | Low to Moderate | Moderate
Thin-Film | Low | Varies | Good | Varies | Moderate to High | Lightweight & Flexible

## Slide 12: Solar Panels
Model | RNG-50D-SS | HQST-50P-US | SP-52-L
Brand | Renogy | HQST | Solbian
Technology | Monocrystalline | Polycrystalline | Monocrystalline
Price | $ 59.99 | $ 65.99 | $ 499.00
Pmax at STC | 50 W | 50 W | 52 W
Voc | 22.3V | 23.3V | 10.9V
Vmp | 18.6V | 19.8V | 9.1V
Imp | 2.69A | 2.53A | 5.7A
Isc | 2.94A | 2.63A | 6A
Weight | 7.7 lbs | 8.4lbs | 1.8lbs
Dimensions (inches) | 22.9 x 20 x 1.2 | 25.9 x 18.6 x 1.2 | 43.7 x 11.49 x 0.1
Temp Coefficient of Pmax (%/degC) | -0.37 | -0.37 | -0.38

## Slide 13: Voltage Regulation
Specifications | Linear Regulators | Switching Regulators |  | 
 |  | Buck | Boost | Buck-Boost
Efficiency | Moderate | High |  | 
Heat | Moderate | Low |  | 
Voltage Output | Step-Down | Step-Down | Step-Up | Up or Down
Output Ripple | Low | Low | High | Low
Complexity | Low | Moderate | Moderate | High
Cost | Low | Moderate | Moderate | High

## Slide 14: Voltage Regulation
Model | LM1085IT-5.0/NOPB | DROK MiniBuck Converter | LM2596 | TPS54JA20
Brand | Texas Instruments | DROK | Texas Instruments | Texas Instruments
Input Voltage | 2.6-26V | 2.5-24V | 3-40V | 2.7–16V
Output Voltage | 3.3 or 5 | 3.3 or 5 | 1.5 to 35 | 0.5 to 5.5V
Output Current | 3A | 3A | 3A | 12A
Price | 2.19 | 1.97 | 1.495 | 0.65
Type | LDO Buck | Buck | Buck | Buck

## Slide 15: Charge Controller
Two broad categories of Solar Charge Controllers:
  PWM
    Basic pulse width modulation
    Lower efficiency
    Cheaper
  MPPT
    Tracks highest power producing operating point
    Higher efficiency
    Typically, more expensive

## Slide 16: Charge Controller
Model | BQ25798RQMR | SR11004 | Adventurer
Brand | Texas Instruments | SMARAAD | Renogy
Input Voltage | 24V max | 26V max | 50V max
Output Voltage | 18.8V max, Programmable | 12/24V | 12/24V
Output Current | 5A | 10A | 30A
Price | 6.25 | 39.99 | 59.99
Power | Not Specified | 260W | 1500W
Type | MPPT | MPPT | PWM
Programming MPPT | I2C | Not Specified | NA
MPPT Type | Sets Voltage to % of Voc | Not Specified | NA
Charge controls | Programmable | Battery Chemistry presets | Preprogrammed depending on chemistry

## Slide 17: Reflectors
Material Chosen to fabricate:
Aluminum has high heat resistance, durable, and high reflectivity in the moon environment.
Mylar increase reflectivity instead of glass which has higher heat change resistance and won’t crack, which reduces quality of refection
Proof of concept: plywood as cheaper alternative and easier to fabricate.

## Slide 18: Motors
Stepper motor: Nema 34 robustness and strong torque to control the rotation of the whole tower. Can be used on DC system
Incorporated gearbox to increase movement range and control for stepper motor.
Servo Motors: a cheaper alternative for smaller part movements.
Types of Motors | DC Brush | DC Brushless | AC | Stepper | Servo
Financial Cost | Small: $5-$50 Medium: $20-$100 | Small: $10-$100 Medium: $100-$500 | Small: $50- $200 Medium: $200-$2,000 | Small: $10-$50 Medium: $50-$200 | Small: $50-$200 Medium: $200-$1000
Size | ~8mm-35mm | ~13mm-35cm | ~10cm-30cm | ~0.4cm-20cm | ~0.4cm-10cm
Torque | 0.36-160 nNm | 4-400 nNm | 203000Ncm-610000Ncm | 10-10000Ncm | 10-1000Ncm
Speed | 5,000 to 14,000 rpm | 100,000 rpm | 1800-3600 rmp | Low | High
Voltages requirement | 4.5V/4.5V/7.0V | 4-24V | 115V/208V/230V | 3V-100V | 3V-100V
Durability | High | High | High | High | Low
Weight | 0.5-160g | 10-1000g | 750g | 150-5000g | 

## Slide 19: Motor Controllers
Stepper Controller DRV8834, cheap and can handle the amperage provided by the system.
PCA9685 PWM: Design specific for servo and can control all three servos planned in the system, compatible with ESP32 C6 and run on I2C protocol.

## Slide 20: Batteries
Specifications | Lead Acid | NiCd | NiMH | Li-ion |  | 
 |  |  |  | Cobalt | Manganese | Phosphate
Specific Energy | 30-50 | 45-60 | 60-120 | 150-250 | 100-150 | 90-120
Internal Resistance | Very low | Very low | Low | Moderate | Low | Very low
Cycle Life | 200-300 | 1000 | 300-500 | 500-1000 | 500-1000 | 1000-2000
Self-Discharge/month at RT | 5% | 20% | 30% | < 8% |  | 
Operating Temperatures | -20 to 50 C | 0 to 45 C | 0 to 45 C | 0 to 45 C |  | 
Maintenance Requirements | 3-6 Months topping charge | Full discharge every 90 days |  | Maintenance free |  | 
Safety Requirements | Thermally stable | Thermal stable, fuse protection |  | Protection circuit mandatory |  | 
Cost | Low | Moderate |  | High |  | 

## Slide 21: Batteries
Model | ML5-12 | HW-4F7 | PQ12V/6AH
Brand | Mighty Max Battery | Howell Energy | Power Queen
Voltage | 12 | 12 | 12.8V
Amp Hour | 5 | 7 | 6
Technology | SLA AGM | LiFePO4 | LiFePO4
Price | 16.99 | 32.99 | 19.59
Temperature Rating | -20 to 50 | -20 to 70 | Not Specified
Weight | 3lbs | 1.9lbs | 1.8lbs
Dimensions | 3.5 x 2.8 x 4.2 | 5.9 x 2.6 x 3.7 | 5.9 x 2.6 x 3.7
Charging Requirements | CV | CC 3.5A, CV 14.6V, Built-in BMS | Not Specified, Built in BMS

## Slide 22: Sensor
 | VL6180X | MAX44009 | SI1145 | VEML7700
Cost (USD) | $14.49 | $5.96 | $9.95 | $4.95
Measuring Principle | TOF/IR Laser Photodiode | Photodiode | IR-LED Photodiode | Photodiode
Max Lux | 100000 | 188000 | 128000 | 120000
Ambient Light Sensing | Yes | Yes | Yes | Yes
IR Sensing | No | No | Yes | No
UV Sensing | No | No | Yes (extrapolated) | No
Operating Voltage (V) | 3 | 3.6 | 3.6 | 3.6
Operating Current (mA) | 0.3 | 0.0003 | 7 | 0.0045
I2C | Yes | Yes | Yes | Yes
SMBus | No | Yes | No | No
ADC | Yes | Yes | Yes | Yes
Size (mm^2) | 234 | 4 | 360 | 15.98
Operating Temperature ( C ) | [-20 - 70] | [-40 - 85] | [-40 - 85] | [-25 – 85]
C/C++ Libraries | Yes | Yes | Yes | Yes
Sensor Final 4 Options:
VL6180X and SI1145 include IR which is not needed
MAX44009 only has breakout board; does not work for PCB
VEML7700 best choice for price/ability

## Slide 23: Comparison and Selection of Software
Vectoring and Positioning / Solar Tracking Algorithm
Communication technologies
Development Environment: Languages and Repositories

## Slide 24: Development Environment: Languages and Repositories
Programming Languages
C: best choice for MCU programming, low-level
Java: best for object-oriented programming, low-level
Python: best for existing libraries, high-level
Choice: C
Repositories
GitHub: most popular repo, widely used among many software devs
Bitbucket: Git based repo, includes task scheduling and team goal software
Choice: GitHub

## Slide 25: Vectoring and Positioning / Solar Tracking Algorithm
Algorithms | Heliostat | Kalman Filtering | Skyview Factor | Ray Tracing | Two-axis Solar Tracking System | Sun tracking Photodiode
Financial Cost | Open Source | Ambiguous | Open Source | Not available | Open Source | No available
Sensor | Ambient Light | Ambient Light | Ambient Light | Ambient Light | Ambient Light | Photodiode
Algorithm code library | Available on GitHub | Available in python | Available on GitHub | Available in Research paper | Available in GitHub | Not available
Efficiency | High | Low | Medium | Medium | High | High
MCU compatibility | Good (C Language) | Fair (Python) | Bad (R Script) | Good (C Language) | Good (C Language) | Bad (No code)
Additional Requirements | Change to an algorithm to change light measuring location | Compass Reading or gyroscopic data |  |  |  | 

## Slide 26: Antenna
 | Dipole | Patch | Reflector (Parabolic) | Yagi – Uda | Helical Antenna | Aperture (Horn)
Gain (dBi) | 1.76-7 | 0.5 -10 | 10 - 40 | 5 – 20 | 3 – 15 | 10 – 25
Polarization | Linear | Linear/ Circular | Circular | Linear | Circular | Linear/ Circular
Efficiency | High | High | High | High | High | Very High
Bandwidth | Narrowband | Wideband | Narrowband | Narrowband | Wideband | Narrowband
Directivity | Omni - directional | Omni - directional | Highly Directional | Highly Directional | Directional | Highly Directional
 | PC140 | WPC.25A | FXP74 | PC17 | FXP70
Average Gain (dB) | -1.92 | -1.14 | -2 | -3.6 | -2
Peak Gain (dBi) | 1.67 | 5.15 | 4 | .9 | 1.1
Efficiency (%) | 64 | 76.9 | 50 | 44 | 63.7
VSWR | <2 | <2 | <2 | <1.5 | <1.5
Polarization | RHCP | Linear | Linear | Linear | Linear
Cost (USD) | $27.26 | $9.21 | $7.69 | $16.60 | $27.09
The combination of the certain gain range, circular polarization, high-efficiency and wideband characteristics made patch and helical antenna types the ideal choices.
The PC140’s circular polarization while also being above average in gain and efficiency made it the preferred antenna product.

## Slide 27: Communication technologies
Criteria | Wi-Fi | LoRaWAN | Bluetooth | 6LoWPAN | Zigbee | Z-Wave
Range (m) | 45 | 15000 | 10 | 100 | 980 | 800
Data rate | 54 Mbps | 50 Kbps | 1 Mbps | 250 Kbps | 250 Kbps | 100 Kbps
Power consumption | 30 uA-250 mA | 1 uA-16 mA | 9 uA-39 mA | 0.3 uA-35 mA | 12 uA- 54 mA | 1 uA-23 mA
Max devices | 255 | 120 | 3-4 | 100 | 100 | 232
Scalability | ✓ | ✓ | ✖ | ✓ | ✓ | ✓
Frequency | 2.4/5/6 GHz | 902.3-914.9 MHz | 2.4 GHz | 2.4 GHz | 915 MHz/2.4 GHz | 908-916 MHz
The combination of low power consumption, suitable range, options for frequency and high scalability made Zigbee the ideal communication technology to implement.

## Slide 28: Hardware Design
Design two separate towers, each with their own design constraints
Majority of focus is on heliostat tower, as it is more complex
Schematics and PCB designs
Heliostat structure
  Tripod on a "Lazy Susan"
Communication Beacon
  Antenna on an enclosure

## Slide 29: Power Delivery/ Electrical Power System

## Slide 30: Stepper Motor Controls

## Slide 31: Servo Motor Controls

## Slide 32: Sensor Control

## Slide 33: MCU System

## Slide 34: Lower-Level Subsystem

## Slide 35: Software Design
Details on software design for the overall system which includes:
Communications through the mesh network
Collecting sensor information
Positioning reflector to deliver sunlight to target
Represented with software diagrams

## Slide 36: Case Diagram

## Slide 37: Activity Diagram

## Slide 38: Motor positioning of Reflector based on light intensity algorithm.

## Slide 39: Motor positioning of Reflector based on light intensity algorithm

## Slide 40: Power Control Algorithm
Component | Essential/Non-Essential | Low-Power Considerations
MCU | Essential | Low-Power Mode, only essential functions
Antenna | Essential | Receive only
Sensors | Essential | Sensors will be turned on periodically
Stepper Motor | Non-Essential | 
Servo Motors | Non-Essential | 
Goal was to reduce power consumption when the sun would not be visible
Reducing usage of non-essential components during these times would preserve battery charge

## Slide 41: PCB Design
MCU
Sensors
Stepper Motor Controller
Servo Motor Controller

## Slide 42: MCU PCB

## Slide 43: Sensors PCB

## Slide 44: Stepper Motor Controller PCB

## Slide 45: SErVo Motor controller PCB

## Slide 46: Administrative Contents
Electrical Engineering | Responsibilities
Alexandre Fiset | PSU Design and Implementation
 | PCB Design
 | MPPT Tracking Implementation
 | Administrative Documentation
Computer Engineering | Responsibilities
Binh Pham | Reflector Technology and Design
 | Motor and Motor Controls
 | Vectoring Technology
 | Project Lead
 | Positioning and Vectoring Algorithm
Computer Engineering | Responsibilities
Pedro Kasprzykowski | MCU Selection and Implementation
 | Software Design and Implementation
 | Antenna and Communications
 | Website Design and Management
Computer Engineering | Responsibilities
Stephen Martin | Sensor Selection and Implementation
 | MCU Selection and Implementation
 | Positioning and Vectoring Algorithm
 | Software Design and Implementation
Distribution of work table

## Slide 47: Mechanical's Budgets
Component | Name | Price/unit | Quantity
Mirror | 0.032" x 24" x 24", 3003-H14 Aluminum Sheet | $28.86 | 1
Mirror Coating | Mylar Sheet | $25.99 | 1
Frame | ADJ LTS-6 T-Bar Tripod Lightweight Lighting Stand | $54.99 | 1
Base Panels | Plywood Panels 4ftx8ft | $25.60 | 2
Communication Tower Box | Junction Box | $26.89 | 1
Wheel Hub Bearing | Rear Wheel Hub | $44.90 | 1

## Slide 48: Electrical’s Budget
Component | Name | Price | Quantity
Battery | Howell Energy hw-4f7 | 32.99 | 1
Motor w | Nema 23 | $30.73 | 1
Motor x-y-z | 9.5-11kg*cm Servo Motor | $17.59 | 3
Charge Controller/BMS | Smaraad SR11004 | $39.99 | 1
Solar Panel | RNG-50D-SS | $49.99 | 1
Microcontroller | ESP32-C6-DEVKITC-1-N8 | $9.00 | 1
External Antenna | Wlaniot 2.4G | $17.98 | 2
MicroSD card | 5251 | $4.50 | 2
MicroSD card breakout board+ | 254 | $7.50 | 1

## Slide 49: PCB’s Budget
Component | Name | Price | Quantity
Microcontroller for PCB | ESP32-C6-WROOM-1U | $3.48 | 1
Stepper Motor Controller | DRV8833PW | $2.84 | 1
Servos Motor Controller | PCA9685PW,112 | $2.64 | 1
3.3V Regulator | TPS54JA20 | $1.50 | 1
5V Regulator | TPS54JA20 | $1.50 | 1
USB-A Connector | 2057-USB-AP-S-RA-SMT-ND | $0.55 | 3
Sensor-MUX | TCA9548APWR | $1.78 | 1
Sensor | VEML7700 | $1.88 | 5
USB-to-UART Bridge Controller | CP2102N-A02-GQFN28 | $4.07 | 1
MicroSD Socket | 1660 | $1.95 | 1
Misc. | Resistors, Capacitors, Inductr, Jumpers, Etc.…. | ~$20.00 |